## Slide 1
Lesson Objectives
            1. Describe what electrical power means and how it is calculated.
2. Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
3. As LO2 , including a change of subject.
Power
Is your work well presented?

## Slide 2: Electrical Power
Achieving Objective 1 - Describe what electrical power means and how it is calculated.
Electrical power is the ____ at which electrical energy is ________by an electric circuit (energy transfer over time). The SI unit of power is the ____, W, (one ____ per second).
Power can be _______ if you know the _______ and ______ difference of a circuit, using the equation:
Power (W) = Current (A) × potential difference (V)
Calculated
Current
Joule
Potential
Rate
Transferred
Watt
rate
transferred
watt
joule
calculated
current
potential

## Slide 3: Electrical Power
Achieving Objective 1 - Describe what electrical power means and how it is calculated.
Electrical power is the rate at which electrical energy is transferred by an electric circuit (energy transfer over time). The SI unit of power is the watt, W, (one joule per second).
Power can be calculated if you know the current and potential difference of a circuit, using the equation:
Power (W) = Current (A) × potential difference (V)
In your own words describe what is meant by electrical power.
How is electrical power calculated?

## Slide 4
Achieving Objective 2 - Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
Power
Power can be calculated if you know the current and potential difference of a circuit, using the equation:
Power = Potential difference × Current (P=VI)
Watt, (W) Volt (V) Ampere (A)
Example: What is the power used in a hair dryer that takes a current of 3 A? Mains voltage is 230V.
P = 3 × 230
P = 690 W
P = V I

## Slide 5: Calculating Power
Achieving Objective 2 - Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
Find the power of a fan heater that takes a current of 6 A.
Find the power of a computer which takes a current of 0.4 A.
A cable can take a maximum current of 3 A, when supplied with a mains voltage of 220 V.
a What is the maximum power that can be carried by the cable?
b How many 60 W lamps, connected in parallel, can be run using the cable?
Which has the greater power, a video recorder transferring 5000 J of energy in 100 seconds or a television transferring 15 000 J of energy in 150 seconds?
Mains voltage is 230V.
P = 230 x 6
P = 1380 W
P = 230 x 0.4
= 92 W
P = 230 x 3 Power = 660 W
660 /60 Number of lamps = 11
5000 / 100 = 50J/s
15000 / 150 = 100J/s. So it’s the TV

## Slide 6
Achieving Objective 2 - Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
Power
Power can also be calculated if you know the current and resistance of a circuit, using the equation:
Power = current squared x resistance (P = I2 R)
Watt, (W) Ampere (A) Ohm, (Ω)
Example: What is the power used in a toaster that takes a current of 3 A with a resistance of 4Ω?
P = (32) × 4
P = 36 W
P = I2 R

## Slide 7
Achieving Objective 2 - Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
Review
What have we found out?
Calculating Power
The cooker has a resistance of 13.0Ω with a 3A supply. calculate the power?
Resistance of 5.5Ω with a 5A supply. calculate the power?
Resistance of 2.6Ω with a 3.4A supply. calculate the power?
power = (3x3) x 13
= 117W
power = (5x5) x 5.5
= 137.5W
Power =(3.4 x 3.4) x 2.6
= 30.1W

## Slide 8
Achieving Objective 3 - Use the equation including a change of subject: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
Calculating Power
Calculate the potential difference when a 16W heater has a current of 4 A?
Calculate the current when a 25W fan has a voltage of 2.6 V?
Calculate the resistance when a 2kW oven has a current of 15.0A?
Calculate the current when a 360W appliance has a resistance of 12Ω?
Challenge: Calculate the resistance when a circuit has a potential difference of 230V and a current of 2A?
P = V x I 16W =P x 4 16/4 = 4V
P= V x I 25W = 2.6 x I 25/2.6 = 9.6A
P=I2R 2000W = (15x15) x R 2000/225=R= 8.9 Ω
P=I2R 360W = I2 x 12 360/12= I2
30= I2 √ 30 = 5.5 A
= 115 Ω

## Slide 9
Check you know the units. Write down the unit for each of these.
Power
Current
Potential difference
Resistance
Plenary
Lesson Objectives
            1. Describe what electrical power means and how it is calculated.
2. Use the equation: power = potential difference × current (P=VI) and power = current squared x resistance (P=I2R)
3. As LO2 , including a change of subject.
Review
What have we found out?
Is your work well presented?